## Slide 1
Amp'ed RF Technology, Inc.
August 6, 2016

## Slide 2: Company Overview
Highlights
  Founded in 2003 in Silicon Valley San Jose CA
  Wireless connectivity provider: WiFi and Bluetooth
  Office opening in Tianjin, China 2009
  Audio/Video Bluetooth SIG Working Group Member
San Jose, CA
R&D and sales support
Tianjin, China
R&D, sales support and manufacturing

## Slide 3: WiFi Connectivity
ACC1340
Amp’ed RF Connectivity Controller
Benefits
Single chip radio solution
Dual Band 2.4 GHz and 5 GHz support
Best in class RF performance
73-pin WLCSP package
Low external component count
Now Available
Features
Dual Band 2.4/5GHz
802.11a/b/g/n
802.11d Regulatory Domain
802.11h 5GHz TPC/DFS
802.11r
21dBm 2.4GHz PA integrated
-97dB Rx sensitivity
Wi-Fi Direct
Soft Access Point
Wi-Fi and Soft AP Concurrent operation
Hotspot 2.0

## Slide 4: Audio Host MCU
ACH1180
Audio Connectivity Host
Analog and I2S audio output
Differential mic input
Floating point processing
Integrated AES encryption engine
Sampling – Q1 2017
Benefits
SoC Host solution: MCU+DSP+CODEC
Supporting CD quality stereo CODEC
Integrated clock management
Cortex M4F, 200MHz
Low power consumption
RF
Serial
ACH1180
I2S/SPI
UART
GPIO
Audio In/Out
832K RAM
Clock
RF Radio
ACC1340

## Slide 5: Embedded Software
WiFi Protocol Stack
Upper layer stack
Embedded RTOS (non-Linux)
Small memory footprint
Optimized for audio applications
OTA – over-the-air software updates
Audio Processing Software
Echo and noise cancellation
Voice filtering and detection
Audio compression
Adaptive playback
Secure audio data AES encryption

## Slide 6: Bluetooth Module
CC2564
Host Controller Interface
ARM Cortex MCU
Including Amp’edUP Stack
UART
SPI
I2C
GPIO
Flash
64K/128K/256K
Clock
RF
Filter
RAM
8K/16K/48K
I2S
BT Radio Chipset
TI CC2564
Host μController
ARM Cortex M4
Bluetooth Protocol Stack
Amp’edUP Bluetooth Stack

## Slide 7: Bluetooth Modules
13.5mm
11.6mm
BT53
Features | BT53
Specification | Bluetooth v4.1
RF chip | TI CC2564
Power class | Class 1
Range | 60m LOS
Dimension | 11.6 x 13.5 x 2.2 mm
Data rate | 500K bps over IAP 1.2M bps over SPP
Interfaces | UART, SPI, I2C, I2S
Bluetooth Dual-mode BT53
Bluetooth SIG Declaration ID: D025845
Bluetooth SIG Qualified Design ID: 65782

## Slide 8: WiFi Modules
Features | 
Specification | 802.11 a/b/g/n
RF chip | ACC1340
Frequency | 2.4GHz/5GHz
Range | 100m LOS
Dimension | 14.6 x 13.5 x 2.2 mm
Data rate | >2Mbps TCP/UDP
Interfaces | UART, SPI
WiFi Dual-band WF43/WF52/WF60
WF60
WF52
WF43

## Slide 9: Product – Development Tools
Data EVB: BT253 Audio EVB SW: Amp’edUP SDK
Classic Bluetooth Stack
Audio Features
Supported Bluetooth v4.1 with A2DP, AVRCP, HFP and other optional profiles
Data Features
Supported Bluetooth v4.1 with SPP, iAP 1/2 and other optional profiles.
Amp’edUP Software Developing Tool
Supported end-user customization of our modules through the use of Amp’edUP SDK

## Slide 10: Bluetooth Stack
Amp’edUP 4.0 Combo
Amp’edUP Bluetooth Stack
Both Classic and Low Energy Options Combined
Features
Classic Profile：SPP, IAP, A2DP, HFP, AVRCP, HID
BLE：ATT, GATT，Prox，Findme，HID，OBEX， Indoor Positioning
Support
Apple MFI
Amp’ed UP SDK
High Quality Audio
End-User Customization

## Slide 11: SonicART
I2S
Spkr/
Headset
Mic
BT Module
Codec
Analog
Analog
Analog
Sonic ART is our proprietary Bluetooth audio enhancement software suite.
Features
  A2DP/HFP profiles supported
  FLECS, Frequency Lock and Error Concealment Sampling
  Sampling rates up to 48KHz, Data rates up to 512K bps
  Acoustic Echo Cancellation and Noise Reduction
  Low Latency Options, <25ms
  Wide Band Speech

## Slide 12: BlueGuard
BlueGuard
BlueGuard is an embedded firmware application layer which runs on top of our exiting Bluetooth Stack & profiles.
Features
Strong Data Security for Payment Card Industries Systems
MIPS FIPs 140-2, Level 3 Data Security Standards
Eliminates Standard Bluetooth Security gaps
Triple DES Data Encryption
Protect Data over public networks!

## Slide 13: Business Model
Technical Support
Stage | Support Available
Wireless system design | Customized support from Amp’ed RF’s engineers.
Hardware design | Reference designs, schematics and layouts, for proven WiFi and Bluetooth modules currently in production.
Firmware integration | Available technical guides: API interface, Generic Kernel/OS interface, Target abstraction layer interface. Working example code is provided.
Regulatory certification | Leverage our partnership with TUV labs for low cost and quick certifications.
Mobile device app development | Example source code available for Android and iOS.
Production | High speed production test software available.